## Slide 1: CAPSTONE PROJECT
OBJECT FOLLOWING ROBOT
Summer 2014

## Slide 2
Supervisor:
  Phan Dung Hung
Authors:
  Trinh Van Quang
  Nguyen Hoang Viet
  Luong Manh Cuong
  Nguyen Binh Duong

## Slide 3: Content
Introduction
Project Management Plan
Project requirements specification
  Non Functional
  Functional
  Tools
Design
  Mechanical Design
  Hardware Design
  Firmware Design
  Software Design
Implement
Testing
Conclusion and perspectives.

## Slide 4: I. Introduction
Idea
Existing product
Scope of project

## Slide 5: 1. Idea
Analysis object behavior
Getting started with Robot

## Slide 6: 2. Existing product
RS4 Robot in Website: http://roboticssamy.blogspot.pt Author: Samuel Matos

## Slide 7: 3. Scope of project
Detect the tennis ball.
Tracking the tennis ball.
Follow the tennis ball.

## Slide 8: II. Project Management Plan
Project process model.
Role and Responsibilities.
Work breakdown structure (Time plan).

## Slide 9: 1. Project process model

## Slide 10: 2. Role and Responsibilities
Supervisor
(Mr.HungPD)
Project Manager (QuangTV)
CuongLM
QuangTV
CuongLM
VietNH
QuangTV
CuongLM
QuangTV
VietNH
VietNH
DuongNB
DuongNB
Analyst Team Design Team Develop Team Test & QA Team

## Slide 11: Work breakdown structure (Time plan)

## Slide 12: III. Project requirements specification
Non Functional
Functional
Tools

## Slide 13: 1. Non Functional
Performance:
  Plug and play
  Battery is enough for 2-3 hours
  Use rechargeable
Maintainability:
  Easy to repair
  Easy to configure

## Slide 14: Non Functional
Reliability:
  Stable software
Safety:
  Components are covered.

## Slide 15: 2. Functional

## Slide 16: 3. Tools
Hardware:
  Raspberry Pi model B rev 2
  Webcam or Raspberry Pi camera module
  Arduino Pro Mini
  L298N Module
  LM2596HVS Module
  SRF04
  R4WD Mobile Platform
  Tower Pro SG90 Servo
  Tiger Power 11.1V 2200mah 25C

## Slide 17
Mechanical devices:
  Knife
  Screwdrivers
  Glue
  Solder machine
  …

## Slide 18: Software tools & enviroment
Arduino IDE, Notepad ++, Geany, Visual Studio.
Raspbian OS, Windows OS, Ubuntu OS.
Microsoft office.
Cmake, V4l2, OpenCV …
Putty, Xming, WinSCP, Terminal Software
…

## Slide 19: IV. DESIGN
Mechanical Design
Hardware Design
Firmware Design
Software Design

## Slide 20: 1. Mechanical design
Control Wheel
Control Camera

## Slide 21: The Standard Driven Wheel

## Slide 22: Forward

## Slide 23: Back

## Slide 24: Turn Left

## Slide 25: Turn Right

## Slide 26: Control Camera

## Slide 27: 2. Hardware design
Power System
Motor System
SRF04
Servo Motor
Raspberry Pi and Arduino
Raspberry Pi and RasPi Camera

## Slide 28: Power System

## Slide 29: Motor System

## Slide 30: SRF04

## Slide 31: Servo Motor

## Slide 32: Raspberry Pi and Arduino

## Slide 33: Raspberry Pi and Raspberry pi Camera

## Slide 34: 3. Firmware design
Firmware dataflow diagram

## Slide 35: 3. Firmware design
Move robot flowchart

## Slide 36: 3. Firmware design
Detect obstacle flowchart

## Slide 37: 3. Firmware design
Turn robot flowchart

## Slide 38: 3. Firmware design
Turn servo flowchart

## Slide 39: 4. SOFTWARE DESIGN
Software dataflow diagram

## Slide 40: SOFTWARE DESIGN
ROI overview

## Slide 41: V. Implement
Programing image process with Pi Eye vision
Pros:
  simple source code to capture object
  Easy to set up and use
Cons:
  usually don’t catch right target
  depend too much on color
  hard to calculate area, because of easy to affect by noise

## Slide 42
Programing image process with OpenCV:
Pros:
  Reliable
  Stable
  Easier to calculate area of object
  Can be consider as almost completed component
Cons:
  Hard to install on RasPi (take 12 hours and easy to get bugged while installing)
  Have to configure a lot to catch object
  Depend on color too

## Slide 43
Programing image process with OpenCV:

## Slide 44
Programing movement control with Arduino IDE :
The process is work good we complete earlier then expect, the Arduino IDE supported everything we need

## Slide 45: VI. Testing
Test Plan
Execute Test
Report

## Slide 46: 1. Test plan

## Slide 47: 2. Execute Test
Test Case ID | Steps | Expected Results | Actual Result | Pass /Fail | Remarks
CRobot1 | Connect Raspberry Pi, Camera and R4WD Running code Place ball in center of camera Moving ball Up slowly | Servo1 will turn up | Good | Pass | 
CRobot2 | Connect Raspberry Pi, Camera and R4WD Running code Place ball in center of camera Moving ball Down slowly | Servo1 will turn down | Good | Pass | 

## Slide 48: 3. Report
No. | Module code | Pass | Fail | Untested | N/A | Number of test case
1 | R4WD, SRF04, Servo | 7 | 0 | 0 | 0 | 7
2 | Tracking Ball | 2 | 0 | 0 | 0 | 2
3 | Control Robot | 4 | 0 | 0 | 0 | 4

## Slide 49: VII. Conclusion and perspectives
Conclusion
  Product:
    Robot running well.
    Components are covered.
  Working in group
    Not good.
Perspectives: